## Slide 1: Maintaining Constructive Interference Using Well-Synchronized Sensor Nodes
Michael König
Roger Wattenhofer

## Slide 2: Constructive Interference (CI)
+
=
+
=

## Slide 3: Traditional Approaches to Transmission Synchronization
Use an external clock.
Don’t send complicated data.
  SlotOS [Flury et al., 2010]
  Black Burst Synchronization [Gotzhein et al., 2011]
Use triggering packets.
  Glossy [Ferrari et al., 2011]

## Slide 4: CI for Broadcasting: Glossy

## Slide 5: Traditional Approaches to Transmission Synchronization
Use an external clock.
Don’t send complicated data.
Use triggering packets.
Can we do it …
… without an external clock,
… with normal data packets,
… and without triggering packets?

## Slide 6: Our Work
General case CI
TelosB
Minimizing error sources:
  Clock synchronization
  Transmission timing
  Travel time
R
SA
SB
S
SA
SB
=

## Slide 7: CI Timing Requirements (IEEE 802.15.4)
250,000 bit/s
4-bit symbols
32 chips/symbol, on I and Q phases in parallel
 1 µs per chip
1 chip
error

## Slide 8: Error Sources
Clock synchronization eclock = clockA – clockB
Transmission Timing etransmit = delayB – delayA
Travel Time etravel = traveltimeB – traveltimeA
Total Error etotal = eclock + etransmit + etravel
Goal |etotal| << 0.5 µs
S
S
=
S
R
S
S

## Slide 9: Travel Time (etravel)
30 meters = 0.1 µs travel time
Workaround: negligible for senders of similar distance
  |etravel| < 0.033 µs
Recent work
  “Time-of-Flight Aware Time Synchronization” (TATS) [Lim et al., 2016]
R
SA
SB

## Slide 10: Clock Synchronization (eclock)
MAC layer timestamping
Averaging out errors
Drift compensation
Combining clocks
Extended precision timestamps
SA
SB
=

## Slide 11: Drift Compensation

## Slide 12: Combining Clocks
2 clocks:
32 kHz quartz
4 MHz DCO (digitally controlled oscillator)

## Slide 13: Combined Timestamp
Virtual High-Resolution Time [Schmid et al., 2010]

## Slide 14: Clock Synchronization Result
|eclock| < 0.05 µs in 20% of cases
|eclock| < 0.25 µs in 75% of cases

## Slide 15: Transmission Timing (etransmit)
Measure: TXON command  SFD pin (“start of frame delimiter”)
(DCO ticks)
S

## Slide 16: Naïve Transmission Timing
if (TargetTime - GetGlobalTime() < 10 ms) {
while (TargetTime > GetGlobalTime())
; // do nothing
cc2420_driver.transmit();
}
22 instructions
165 instructions

## Slide 17: Split Clock Transmission Timing
void await(uint64_t local_target) {
uint16_t target_tarof = (local_target >> 23) & 0xFFFF;
uint16_t target_tar = (local_target >> 7) & 0xFFFF;
while (TAR_overflows < target_tarof)
;
while (TAR < target_tar)
;
uint16_t target_tbr = (local_target & 0x007F) + TBCCR6;
while (TBR < target_tbr)
;
}
await(GetLocalTime(TargetTime));

## Slide 18: New Loop Size
.L24:
mov &__TBR, r15
cmp r12, r15
jlo .L24
; 3 cycles
; 1 cycle
; 2 cycles
New maximum error: 6 cycles

## Slide 19: Loop Alignment
switch ((target_tbr - TBR) % 8) {
case 7:
_NOP();
case 6:
_NOP();
case 5:
_NOP();
case 4:
_NOP();
case 3:
_NOP();
case 2:
_NOP();
case 1:
_NOP();
case 0:
default:
;
}
while (TBR < target_tbr) {
_NOP();
_NOP();
}
New maximum error: 1 cycle!
and #7, r15
rla r15
br .L34(r15)
.L33:
nop ; 1 cycle
.L32:
nop ; 1 cycle
.L31:
nop ; 1 cycle
.L30:
nop ; 1 cycle
.L29:
nop ; 1 cycle
.L37:
nop ; 1 cycle
.L47:
nop ; 1 cycle
.L45:
mov &__TBR, r15 ; 3 cycles
cmp r12, r15 ; 1 cycle
jlo .L37 ; 2 cycles
the jump table (omitted)

## Slide 20: Summary of Error Sources
|eclock| < 0.25 µs (in 75% of cases)
|etransmit| < 0.25 µs = 1 cycle
|etravel| < 0.033 µs = 10 m/c
|etotal| = |eclock + etransmit + etravel| << 0.5 µs
!

## Slide 21: Excursion: The Capture Effect

## Slide 22: Excursion: The Capture Effect

## Slide 23: The Capture Effect – Power Difference
[“Sharing a Medium Between Concurrent Protocols Without Overhead Using the Capture Effect”, 2016]

## Slide 24: Results: Example A

## Slide 25: Results: Example B

## Slide 26: Results with 3 Senders
RSS1 – RSS3 [dB]
RSS2 – RSS3 [dB]

## Slide 27: Results with 3 Senders
RSS1 – RSSavg [dB]
Var(RSS>1) [dB]

## Slide 28: Results with 4 Senders
RSS1 – RSSavg [dB]
Var(RSS>1) [dB]

## Slide 29: Results: Ground Truth

## Slide 30: RSS Gain

## Slide 31: Summary
; 3 cycles
; 1 cycle
; 2 cycles
.L24:
mov &__TBR, r15
cmp r12, r15
jlo .L24
+
=
|etotal| = |eclock + etransmit + etravel| << 0.5 µs
!

## Slide 32: Questions
Michael König